# RACING - SEAT & HARNESS

# From: Mahler9th@aol.com

To: JAPasha@aol.com

Subject: Safety Harness Installation

Jim Pasha's recent Excellence Tech Forum article (August '97 issue) on safety shows some pictures of the inside of my cars '87 951.

Anyway, Jim did not include two key points regarding the mounting of safety harnesses:

(1)	If you have a late model 944/951 and you use the factory seats, you will not have a convenient location for mounting the inside lap belts.  On the early cars, you can use the factory lap belt location, and have your safety harness and your stock belt share the convenient threaded hole in the tranny tunnel.  On the later cars, the inside stock seat belt is actually bolted to the seat.  It is not considered safe to mount a safety harness lap belt to the seat.  You may be able to get away with this for AX, but I don't think it would be safe for the street or the track.

On my car, which is an '87 951, you can see in the photos that I have a pair of Recaro seats.  I had to solve the lap belt problem when I put these seats in to even use the stock street belts, since I couldn't attach them to the seats. I had to drill a hole in the tranny tunnel to mount an eye bolt (of course with a back-up washer and lock nut), and mount a street-version seat belt receptacle. When I drive on the street, I use this receptacle with the factory belt system. On the track and for AX, I clip in the TRW/Sabelt inner lap belts that you can see in the photos.  The drilling process was pretty easy, and the holes are not cosmetically unattractive.

(2)	You don't have to drill a hole in the floor for your anti-sub belt.  I use a ~2-2/12" wide strip of 3/16" thick steel which stretches across the front seat rail mounting bolts.  Thus, the two bolts which hold down the front part of the seat rails sandwich this bracket between the car and the bottom of the rails. My anti-sub belt is then attached to the middle of this simple bracket.  The anti-sub belts are positioned correctly to prevent submarining.  I use slightly longer-than-stock high grade bolts to hold down the seats and the brackets to accomodate for the thickness of the bracket (3/16").

Of course, before you mount any belts, make sure that you read all instructions and cautions provided by the manufacturer, and check the rules in force by your club or sancioning body.

As many of you know, I had a shunt at Laguna in my first 951 (an '89 with 31k miles).  The belt system and seat worked well, although the Weltmeister harness bar I had at the time was slightly bent, I was completely uninjured and unmarked. Wasn't even sore.  I hit a wall at maybe 40 mph almost head on.

# M. Mitchell

----------

# From: paul.foster@micromuse.com

Subject: Re: 951 Harnesses

I've heard of others attaching sub belts this way, but I think the sub belt needs to be mounted at or behind your crotch to be totally effective. Running the belt over the front of the seat is giving you a decent amount of room to submarine. I still think the best approach is to use a 6-pt. system and attach the anti-subs to the same points you mount the lap belt. Some organizations, such as the SCCA think you should use different mounting points, but I simply don't see the need. If you lose one of the lap belt mounting points, your antisub belt isn't goind to do you *any* good!

(Bending the harness bar) is *very* distressing. I had initial fears with the flimsiness of the Weltmeister (aka Automotion!) harness bar. Now I have some empirical data. What if your accident had been at 80? E=m*v*v. I hate to go to the expense of a Brey-Krause, but it looks like there is no other safe choice except to install a roll bar/cage.				Paul Foster

----------

# From: zmf@uwyo.edu  (Z. Fuzessery)

Subject: re: safety harness

Or you can mount the submarine belts on a 6-pt. to the front bolts on the seat rail, w/out adding the x-bar. Haven't had a wreak, but seems secure.	Nick

---------------------------------------------------------------------------------

# From: lee@pmsales.com  (lee)

Subject: Re: Slotting Seats

As I posted some time ago, there is yet another alternative.  Dave Turner (long time national autocrosser) makes and sells what he calls a "Harness Holding Strap", to work in conjunction with the Porsche high-back sport seats.  It is designed to help keep the shoulder harnesses from slipping off your shoulders. It is best used with some type of harness bar.  Cost is about $25.  For more information, you can request his catalog by contacting:

Performance World

San Diego, Ca

800-854-6640

619-571-3811 (current a/c in '92-might have changed)

619-571-2859 (fax)							Lee Lichtenstein

---------------------------------------------------------------------------------

# From: barry.lenoble@peri.com  (Barry Lenoble)

To: bbechtold@smartcamber.com

Subject: Re: Seats for club racing

>So, are one-piece lightweight racing seats legal in the Prepared class???  I >really prefer them over the expensive Recaro SRD and such...  So, what is legal?

----------

According to the PCA Club Race Rulebook:

6. Body/Chassis/Interior

F. Seats are free providing minimum weight of vehicle is met.  Any ballast to meet weight must be places entirely in the driving compartment and must be securely bolted to the chassis.

So yes, one piece lightweight racing seats (like Kirkey, ButlerBuilt, etc.) are legal. Note that racing seats, with harness slots, are STRONGLY recommended.

# Barry Lenoble, barry.lenoble@peri.com, 89 944 Turbo

---------------------------------------------------------------------------------

# From: Jason Burkett paragon@interconnect.net

Subject: Re: 5-Point harness

At 02:04 PM 11/27/97 -0500, you wrote:

>I have a '86 951 used as a daily driver and for monthly time trials.  I just >purchased a Sparco racing seat to exchange for time trials since the shoulder >belts don't fit well around the stock seat.  After mounting the seat and >adjusting belts, I find that cinching the shoulder belts tightens the submarine >belt uncomfortably against my groin.  What do racers do?

----------

Ummmm....quickly determine if they are a "lefty" or a "righty". When your voice goes up an octave they are usually tight enough. Seriously, you may try tightening the lap belts first. The sub strap should be adjusted so that it it pretty slack free at this point (i.e. tight). Then tighten your shoulder straps.

# Jason Burkett, Paragon Products

----------

Most of them use a double sub-strap.

# From: "Andrew Warren" fastfwd@ix.netcom.com

----------

You may need to shift the mounting point for your anti-sub belt.  The belt is there to keep the lap belt from riding over your illial crest in an impact.  It's not there to directly hold you into the seat, nor is it there to force your testicles to reascend into your abdominal cavity.

# Kevin Gross, kgross@connact.com

---------------------------------------------------------------------------------

# From: lee@pmsales.com (lee)

Subject: Re: Harnesses and camera

Todd Leen <tleen@auslese.cse.ogi.edu> wrote:

>1)  Harnesses -- for now, I'd like to keep the stock seats in the car.  What's >a good harness arrangement ? I intend to mount the shoulder harness to the roll >bar's harness bar.  Seems like the shoulder harness is likely to spread apart >having to wrap around the sides of the stock seat.  What's the fix?

----------

For about 10 years or so, I have been using a product made by Dave Turner (world class auto-xer).  He calls it the "Harness Holding Strap", and he designed it primarily for the Porsche Hi-Back seats.  The price was about $25 back in '92. I don't think it would be more than $30 now.  You can contact:

Performance World (was known as Dave Turner Motorsports)

# San Diego, CA

800-854-6640

619-571-3811 (CA, AK, HI)

619-571-2859 (fax)

I use it in conjunction with 2" H-type harness attached to a regular harness bar, and have never had any problems with it on any of my cars ('83NA; '88 TS; '93 968).  Be prepared to make a color selection.  Don't get this confused with the infamous "Torso Harness", which is a single strap that wraps around your chest.

It is made of the same material as the 2" shoulder harness, and has a clamp for adjustment.  You slip it over the headrest and tighten it at the height you desire.  There are two "loops" sewn to it, positioned so that once installed, one loop will end up over each shoulder.  You simply feed the shoulder straps thru the loops.  The loops also prevent the shoulder harness straps from falling down on the floor and help to keep them up on your shoulders where they belong.

# Lee Lichtenstein Lee@pmsales.com

---------------------------------------------------------------------------------

# From: Gunmspt Gunmspt@aol.com

Subject: seats with slots

From my personal experience, most "Porsche seats can be modified for seatbelts using simple hand tools & purchase of "slot receivers" from Corbeu USA.  The receivers are under $10.00 each.  I have modified my 911 seats for shoulder harness & crotch belt (3 slots) & 914 seats for the crotch belt.		DCNTHER

---------------------------------------------------------------------------------

Subject: Re: Drilling for Harness belts... Where exactly? 3/10/99L

# From: "Claus Groth" bora450@gte.net

Eric wrote:

<< I am in the process of installing 6 point harnesses in my 944, and I have decided that the inboard lap/substrap belt mount must be drilled, and have an eye bolt installed (rather than use the factory seat point). Has anyone on this list done this operation, and if so, any tips as to where exactly the mount should be located on tunnel? >>

----------

I installed an eyebolt in the floor, five inches behind each seat rail.  This allows the stock seat to be adjusted fully back without hitting the eyebolts and is the correct location for the belts to angle forty-five degrees forward to my racing seat belt holes.  It is difficult to mount an eyebolt in the side of the tunnel due to the heat shields installed underneath and also there is insufficient room between the seat and the tunnel for an eyebolt.  Be sure to install large washers under the floor to distribute the load.  Even better would be a strap connecting the two eyebolts.

Subject: Re: Seatback brace, 2/8/99R

# From: Walter Fricke <FrickeW@ci.boulder.co.us>

Here it is.  I’ve copied it into the text, since attaching it doesn’t always work, it appears:

PCA Club Racing now requires a seat back brace.  The only specification given is that there be 12 square inches of contact surface between the brace and the seat back.  Obviously, such a brace, in order to do its job if needed, needs to be sturdy.  In a full out race car you have lots of design freedom.  In a street car you probably want the brace to be easily adjustable, or perhaps better yet, removable.  The SC Kathy races (and I drive daily, and occasionally use on the track if the GT car is ailing) has an Autopower roll bar.  This bar has no horizontal cross brace.  It has a steel strap joining the diagonal cross brace, but this is way too far back to serve any useful function in my car.  In addition, the SCCA (as I read their rules - perhaps I am incorrect about this) requires that a seat back brace be *attached* to the seat back to prevent the seat from collapsing sideways.  It seemed to me a good thing if you could combine lateral support of the upper seat back with its main function of resisting movement to the rear.

I have a Recaro SRD in the car, which I have had since 1992.  Fine dual-purpose seat, in my experience.  I didn’t really want to drill holes in it.  While I have concluded that the seat back is made of steel stampings and some steel tubes or rods, I didn’t want to remove all its upholstery to find out how it is made and where a connection could be made.  In fact, I didn’t want to attach anything to this seat, and I want to be able to bend it forward in the usual way for access to the rear seat area.  Here is what I came up with for the brace:

Take a length of one-inch angle iron at least 17=22 long. Make a straight cut in what will be the horizontal part so you can bend a one-inch tab at 90 degrees. Make a similar cut toward the other end, leaving 14 1/4 inches between the two tabs.  Cut filler pieces to go in the V spaces left in the horizontal part after the bend, and weld them in.  You now have an angle iron brace that will span the rear of the seat.  The wings or fingers at the end, which retain their angle iron shape, will reach forward along the sides of the seat just above the seat back release for an inch and prevent the seat from moving sideways without interfering with the release.  And you will have 14 plus square inches of bearing for the rear loads which is below the shoulder strap holes, but high enough to do a good job of supporting the seat back.  In addition, this part of the rear part of the seat is flat.  You should, of course, measure your seat before making anything. All Recaro*s may be the same dimensions here, and then they may not be.  Also, I made the mistake of making mine a bit too narrow on the first try.  Had I made it a bit too wide I could have simply put filler pieces in on the sides to make it a snug fit.

That accomplished, the next task is to support the brace to the roll cage or bar. There are many ways to do this, but here’s what worked for me.  I think Autopower makes an *add on* cross bar for their cage.  This might do well, but I decided I would make my own cross bar, and locate it forward of the roll bar and fairly close to the seat back.  This reduces the bending forces on whatever connects the bar to the brace.  So I got a piece of tubing of inch and a half tubing, and had a shop bend it so its ends curved in to meet the roll bar vertical on one side, and the diagonal on the other side, with a straight section in the middle, to serve as a support tube.  I welded two long 10mm bolts onto the brace so they stuck straight back and were located about a third of the way in from each end.  Where they were to go through the tubing piece I drilled oversized holes and welded short tubes with about an 11mm ID through the tubing. When you mount anything by bolting through a piece of tubing you want to do this, so tightening never tries to collapse the tubing.  When Kathy uses the seat I put a thick walled tubular spacer about an inch long over the bolts and up against the brace.  I then push the bolts through the support tube and tighten nuts on the other side.  For me the seat comes back one notch, so I take the spacers out so the brace is close to flush with the support tube, and put them on the other side under the nuts.

This brace also has to attach to the roll bar.  The diagonal bar, of course, slants at about a 45-degree angle.  My Autopower roll bar is a floor mount, and as the down tube rises from the floor it bends out toward the side of the car slightly.  My first thought was to construct flanged clamps that would be held together with bolts on each side.  This is how removable bars in a cage system are usually attached.  Looking at things, though, it became clear that the forces were all going to be toward the rear at angles which would generally force the support tube into the cage bars to which it would be mounted.  So I cut a short piece of cage tubing in half and massaged these so each half would fit onto the OD of the cage bars.  This was long enough so its ends stuck out on each side of the support tube with enough room for a hose clamp.  I then put everything in place, and after some fitting welded the ends of the support tube to the clamp pieces.  Because the diagonal roll bar support is at such an angle that there would be a significant force vector pushing that end of the support tube down, I welded a stop onto the diagonal roll bar at that point (the only thing I had to do to the roll bar).  This is all held in place by four hose clamps, but all they have to do is keep the support tube from falling by its own weight.  Any side or rear forces are going to be transferred to the roll bar tubing at close to a perpendicular (aided by the stop on the diagonal bar so things aren’t pushed down it).  It is the work of maybe a minute to mount or dismount the whole assembly.

If I get energetic I may still convert this to a conventional flange clamp or, going half way, a double U bolt setup.  That might do an even better job of retaining the rear protection integrity of the seat brace even if some other component of the crash distorts the roll bar, and still be pretty easy to put on and take off.

I think one might be able to purchase a clamp-on cross bar ready made from Autopower (they, or one of their vendors, even has a web site where one can glean additional information).  If this locates at the right height it would be worth looking into.  I like my system because by bending the cross bar forward I don’t have any long, spindly support braces.  The longer such pieces are the more susceptible to buckling and bending sideways under loads they are, so keeping them short and almost entirely in compression avoids those issues.  But with a little thought something easier to fabricate (getting the end notches right isn’t easy) could probably be fashioned starting with a manufacturer’s piece.

Subject: Re:  out of date race harness, 4/8/99L

# From: "Mike Green" mikegreen@pcola.gulf.net

# Pegasus or Racewholesale will reweb them for $79.

Subject: Re: Seat back braces, 4/12/99R

From: Paul Foster pfoster@gdi.net

http://www.ioportracing.com  They have two models for $65. I use the I/O Port one. Tell Ken Myers I said hi!						Paul Foster

----------

Pegasus' catalog has them.  Around $60.					Jon Lowe

Here are a few of the more unusual/interesting items they suggest

looking at:

"Severe overheating can often damage a good thermostat. If the

engine has overheated because of another problem, the

thermostat       should be tested or replaced before the engine is

returned to

service."

"Sometimes a lower radiator hose will collapse under vacuum

at          high speed and restrict the flow of coolant from the

radiator

into the engine."

"Dragging brakes - A caliper thats sticking or a parking

brake          that isn't releasing may be making the engine work too

hard."

_______________________________________________________________

Get Free Email and Do More On The Web. Visit http://www.msn.com

----------------------------------------------------------------------

Subject: Re: Club Racing minimum (long)

From: "Barry Lenoble" <lenobleb@symbol.com>

Date: Mon, 26 Apr 1999 16:13:59 -0400

X-Message-Number: 94

Hello,

-----

<<<Again, for myself I started coming down to earth when I realized the

$$$ involved in getting Club Race-ready!  Just to start:  transponder=20

(required), track wheels and tires, competition shocks, etc...  And

then, to be competitive is a whole different story.  Hmmm, I'll perhaps

need a trailer, tow-vehicle, bigger garage (with a drain this time) for

the extra vehicles and equipment, etc....>>>

Not true. The transponder is actually optional but you do need one to be

timed. That means you will always start from the back. R tires are also

not required, although I think you really want them. But you _could_ use

your OEM wheels... Barry Lenoble went club racing on an incredibly small

budget. It can be done. But being out there is much better than sitting

=AF-----

It's true, you don't have to spend a fortune to go racing (although it =

does

help). My first year, I bought a roll bar for $300, a driving suit for =

$70, nomex

undies for $100, a kill switch for $50 and window net for $30, and the=20

net mounting kit for $15. I already had a hemlet, gloves, and shoes.

You don't need track wheels, special shocks, tow vehicle, etc. I did =

two=20

races my first year by packing my car full of stuff and driving to the =

track.

I raced on BFG R1's, which were sticky enough on the track, and safe

enough to drive on the street (unless it rained too hard). I even brought

a tent and slept in that for the first race (and I froze my =AF- off at =

Lime Rock

in April).

----

<<<7.      Seat meets rule requirements>>>

You need a seat with shoulder harness cutouts as a minimum. You can get

aluminum racing seats for less than $200. A Recaro SRD which allows you

to drive the car on the street without killing yourself costs $600. But

you can always swap out the seat...

=AF--

As you know, the seat rules have changed, and now you need a dedicated

race seat, and a seat back brace. However, as Paul writes, you can get one

pretty cheaply. A Kirkey Economy seat is $130, aluminum mounts are $50,=20

and a brace is $50.

Other costs have gone up too, you now need an SA95 helmet, the $210

transponder, and some other stuff. However, if you're heavily into driver

ed, then the additional costs to go racing are pretty minor, and are

easily rationalized (safety first, right).

Since I started racing, I have obtained another set of wheels, a tow =

vehicle

and trailer, but you don't HAVE to do that. In fact, if Bridgehampton were =

still

open, I would not have bought the rig (I live less than 1 hour from the =

Bridge

and did most of my driving there, now that it's gone, I have to travel =

further

to play).

Note that my car is still pretty much stock, I have changed the swaybars =

to

club sport parts (30mm front, 20mm rear) and I've removed the cat, and

I have the race seats, but my springs, shocks, torsion bars, A -arms, =

bushings,

muffler, etc. are all stock. I'm not the fastest one out there, but I am =

competitive.

> I only have one word of advice: If you even _think_ you might want to do

> this, do it! That is as long as you have some track time under your belt

> and you are at least in the intermediate DE group. The big issue is

> situational awareness. Cars can pass you at any time and they do. I have

> been on the track with a 962. Turn into someone and it will ruin both of

Here's where I have a slight disagreement with Paul. Racing is a blast,=20

and you may want to give it a try. However, before you do, ask yourself

if you're prepared to have your nice shiny car wadded up into a ball.

What would you do then? If you can't handle that thought (and more =

important

the loss of money you have in the car), then you should not go racing.

Although the chances of it happening are slight, they are there, and I've

seen enough totalled cars. Note that some people do purchase insurance=20

that covers you when you race, but it was too expensive for me.

So think about it, and if you want to come play, we'd love to have you.

Barry Lenoble

lenobleb@symbol.com=20

89 944 turbo, Alpine White

----------------------------------------------------------------------

Subject: Hottest Porsche in india

From: "MT" <martin.taylor@clear.net.nz>

Date: Tue, 27 Apr 1999 08:02:19 +1200

X-Message-Number: 95

Have you checked the AFM against the specs, if it wasn't giving the correct

readings it could cause a lean situation (up to 3600 RPM) what do you think?

Martin

----------------------------------------------------------------------

Subject: RE: SP8000 and tramlining

From: "Menelaos N. Karamichalis" <menelaos@starnet.net>

Date: Mon, 26 Apr 1999 16:09:37 -0500 (CDT)

X-Message-Number: 96

I have received a couple of responses on my question which have prompted

me to amend to my original query:

On the front of my 951, I have replaced a set of 7"x16" wheels w/

205/55/16 tires and 23mm offset w/ a set of 7"x16" wheels w/ 225/50/16

tires and 53mm of offset.  Thus, I have increased the tire width but

actually decreased the front track width and I can affirm that visually.

Would the track width reduction alter the alignment settings?  I would

think not.

Or could it be that the new track width is exactly right to make my car

follow truck ruts whereas the old one was not?  On some roads, the car

behaved perfectly, on some I had to keep the steering wheel slightly off

center to keep the car going straight.  Very tiring.

Once more, thanks.

Menelaos N. Karamichalis	mnk@verio.net	www.starnet.net/~menelaos/

Zone 10, St. Louis Region PCA member		Diamantblau 1987 951

----------------------------------------------------------------------

Subject: ClubSport logo

From: "berloth" <berloth@publishnet.nl>

Date: Mon, 26 Apr 1999 21:43:29 +0200

X-Message-Number: 97

Hi List,

It took a while, but I got the ClubSport logo (as on the side of the 968

CS) in vector format. This means you can take this file to your local

car-decal shop to have 'em "die-cut"

For those who are intrested, lemme know, I'll send 'em to ya...

Happy Porsching

Jeroen - the Netherlands

911carrera coupe '87

----------------------------------------------------------------------

Subject: Re: Club Racing minimum (long)

From: Steve <A951S@banet.net>

Date: Mon, 26 Apr 1999 17:58:10 -0400

X-Message-Number: 98

>It's true, you don't have to spend a fortune to go racing (although it does

>help). My first year, I bought a roll bar for $300, a driving suit for

$70, nomex

>undies for $100, a kill switch for $50 and window net for $30, and the=20

>net mounting kit for $15. I already had a hemlet, gloves, and shoes.

>

>You don't need track wheels, special shocks, tow vehicle, etc. I did two=20

>races my first year by packing my car full of stuff and driving to the=

track.

>You need a seat with shoulder harness cutouts as a minimum. You can get

>aluminum racing seats for less than $200. A Recaro SRD which allows you

>to drive the car on the street without killing yourself costs $600. But

>you can always swap out the seat...

>=AF--

>

>As you know, the seat rules have changed, and now you need a dedicated

>race seat, and a seat back brace. However, as Paul writes, you can get one

>pretty cheaply. A Kirkey Economy seat is $130, aluminum mounts are $50,=20

>and a brace is $50.

>

>Other costs have gone up too, you now need an SA95 helmet, the $210

>transponder, and some other stuff. However, if you're heavily into driver

>ed, then the additional costs to go racing are pretty minor, and are

>easily rationalized (safety first, right).

>Note that my car is still pretty much stock, I have changed the swaybars to

>club sport parts (30mm front, 20mm rear) and I've removed the cat, and

>I have the race seats, but my springs, shocks, torsion bars, A -arms,

bushings,

>muffler, etc. are all stock. I'm not the fastest one out there, but I am

competitive.

Big question, do you need all this stuff for Drivers Ed?

I thought you just needed the SA95 helmet.

I was thinking of doing some Auto-X and Drivers Ed

but nomex suits and specialized seats etc...???

Am I missing something here?

TIA

-Steve

----------------------------------------------------------------------

Subject: Need Hella Lights

From: BRADB944@aol.com

Date: Mon, 26 Apr 1999 18:12:30 EDT

X-Message-Number: 99

Help me please Listers.  After reading a post about this upgrade and talking

to the poster.  My thanks to Chris for the info.  I was all fired up that I

know how to fix my weak lighting on my 83 944.  Chris is running Hella's Euro

driving/fog with 55/100 watt bulbs.  Pretty sure that's what he told me,

correct me if I'm wrong.  All excited, I called my guy at the parts place

that I usually deal with and got less than expected.  "Well, we have a

catalog around her someplace, but it's 3 years old.  Call ya back when I find

it"  Called me back and told me he thinks he's found what I'm looking for.

$65.00/side.  My two back up parts places were even less help.  So, plan B,

mail order, wrong! Girlfriend when she was helping remodel the living room

did something with all my parts catalogs, life is good isn't it?  Can

somebody please help me out here.  Need part numbers, prices and a supplier

where I can get these.  I'm in the sticks of southwest Michigan in the dark.

Please somebody.......Let there be light!

Thanks

Brad

----------------------------------------------------------------------

Subject: Re: Club Racing minimum (long)

From: lee@pmsales.com (lee)

Date: Mon, 26 Apr 1999 17:27:19 -0500

X-Message-Number: 100

A951S@banet.net wrote:

>Big question, do you need all this stuff for Drivers Ed?

>I thought you just needed the SA95 helmet.

>I was thinking of doing some Auto-X and Drivers Ed

>but nomex suits and specialized seats etc...???

>Am I missing something here?

>TIA

>                            -Steve

A lot of it depends on whose running the event and what class you end up

running in.  For example, in Chicago Region Track DEs, the minimum

requirements are:

Novice Class (group 4) - OEM seats, 3-pt OEM seatbelts, SA90 helmet, long

sleeve cotton shirt, long pants, socks, all made of non-synthetic material,

and closed toe shoes.

Other Classes (groups 1, 2, 3) - OEM seats, 5 or 6-pt harness mandatory for

driver, and, if you wish to have an instructor ride with you, the same type

of harness is required on the passenger's side.  Plus, the same

helmet/clothing rules as with group 4.

Recommended, but not mandatory, are driver's suits, driving gloves, driving

shoes, and a protective neck brace all made of Nomex or similar

fire-resistant materials, as well as a mounted fire extinguisher.

Full racecars (usually running in groups 1 & 2) are usually already

equipped with additional safety items (rollbar or cage, window net, cutoff

switch, fire system, dedicated race seat, etc.).

The best thing to do is contact the event chairman or safety chairman for

the particular event in which you wish to participate..........generally,

there are no "hard and fast" rules from region to region (except for

Parade).

Lee Lichtenstein <Lee@pmsales.com>

PCA/Chicago (permanent region car #44)

'93 968 Coupe (Nachtblaumetallic/Cashmere)-107k miles

'99 Porsche Parade Entrant #213

----------------------------------------------------------------------

Subject: The Rocket... & Power/weight ratios

From: Jim Demas <JDemas@earthlink.net>

Date: Mon, 26 Apr 1999 15:30:56 -0700

X-Message-Number: 101

After seeing The Rocket yesterday (see post yesterday) just scream through

some esses... I got to thinking about the power to weight ratios of a

number of cars...

car			weight	hp	ratio lbs/hp

The Rocket... 		814	143	5.692

911 Twin Turbo		3490	400	8.725

Porsche 911 (996)		3080	296	10.405

Porsche 951S		2998	250	11.992

Graham Gillies'944T (est)	2998	500	5.996

Ferrari 550 M		3725	485	7.680

Lamborghini Diablo SV	3365	530	6.349

ViperGTS		3380	450	7.511

Pretty damn impressive, I'd say.   Also.. the Rocket has 11" Brembos in

front and 10.5 in the rear... think it stops great?!  Though the stated

acceleration figures on their website are just 4.4 and 10.01 to 60 and 100

respectively...  these must be the most conservative figures I have ever

seen.  This car is faster than that.. and through the corners.. I am not

sure anyone could keep up. No kidding.   You had to be there and see the

car to believe how quick it was accelerating and going through the corners.

Bryce and I were amazed...

So... I am on a diet today.  I need less weight.. and more hp.

-- Jim

Jim Demas

Hillsborough, California

(650) 579-1407

1991 S2 Coupe... KristallSilberMetallic/Black

----------------------------------------------------------------------

Subject: Re: BB idler adjustment

From: JoeJack951@aol.com

Date: Mon, 26 Apr 1999 18:39:07 EDT

X-Message-Number: 102

I thought it was 1 mm interference with the belt. That's how I set mine and I

didn't notice any abnormal whining. Then again I only drove the car 40 miles

before I decided to replace my head gasket.

Joe Jackson '86 951

still headless

In a message dated 4/26/99 1:36:53 PM Eastern Daylight Time,

blackbox@san.rr.com writes:

> HI Phillip,

>

>  I just did mine.....the idler should have a 1mm (I belive) gap between it

> and the belt. Loosen

>  the idler nut, you'll need a flat wrecnh to hold the lock down

nut...(Claus

> built a real cool

>  tool by buying a cheap wrench and machining it flat...works

great!)...losen

> the idler bolt, gap

>  the roller then hold the lock down nut and tighten the toller nut.....if

> your gap is too close,

>  yur car will sound like a blown V8.....scares the ricers...but scrared me

> too :-)

>

>  John,

>  87 951 Blk/Blk

>  http://home.san.rr.com/myzone

----------------------------------------------------------------------

Subject: Re: Synthetic Oil

From: "Nabi" <nabi@vill.com>

Date: Mon, 26 Apr 1999 18:2:38

X-Message-Number: 103

15W-50 would be better in the hot summer months.

On 04/26/99, ""alex loureiro" <alexloureiro@email.msn.com>" wrote:

> Living in the northeast where the temp varies by season, what grade mobile

1 should be used. In the summer months is 15w-50 the choice or is 10w-30 a

better one?

Alex-'88 944 Turbo S

----------------------------------------------------------------------

Subject: Re: Club Racing minimum (long)

From: Paul Foster <pfoster@gdi.net>

Date: Mon, 26 Apr 1999 19:03:39 -0400

X-Message-Number: 104

Barry Lenoble wrote:

>

> Other costs have gone up too, you now need an SA95 helmet, the $210

> transponder,

Yes on the helmet, no on the transponder. You can rent it, borrow it, or

go without.

> > I only have one word of advice: If you even _think_ you might want to do

> > this, do it! That is as long as you have some track time under your belt

> > and you are at least in the intermediate DE group. The big issue is

> > situational awareness. Cars can pass you at any time and they do. I have

> > been on the track with a 962. Turn into someone and it will ruin both of

>

> Here's where I have a slight disagreement with Paul. Racing is a blast,

> and you may want to give it a try. However, before you do, ask yourself

> if you're prepared to have your nice shiny car wadded up into a ball.

> What would you do then? If you can't handle that thought (and more important

> the loss of money you have in the car), then you should not go racing.

> Although the chances of it happening are slight, they are there, and I've

> seen enough totalled cars. Note that some people do purchase insurance

> that covers you when you race, but it was too expensive for me.

Oops! I forgot that part! Of course, you have to pony up to the idea

that your daily driver and/or favorite toy may be going nowhere ever

again... You also have to consider the personal risk. I don't have a

wife and kids so that part is pretty easy for me.

Paul Foster

----------------------------------------------------------------------

Subject: Re: a-arm ball joints

From: "Nabi" <nabi@vill.com>

Date: Mon, 26 Apr 1999 18:11:26

X-Message-Number: 105

Eric,

put the car on a lift, or jack up the car as safely

as you can (this is much easier if you have access to

a lift)

grab hold of the bottom of the tire and move it back

and forth pretty hard, while keeping your eye on the

pin and the ball joint. if you see or feel any movement,

I would change them.

rebuilts may be good for street, I don't have sufficient

data to propose them for track use. I would also replace

both at the same time. the other arm is just as old as the

one that's broken, unless you have infomation to the contrary.

just being safe.

good luck,

nabi.

On 04/26/99, "Eric Dorman <eric.l.dorman@cpmx.saic.com>" wrote:

> i am replacing oil-rotted rubber parts on from suspension

> of '86 951 (mileage unk. but not low (flakey odometer)).

>

> how does one know whether the ball joints are worn

> enough to replace?

>

> one (right side) is tight (almost unmovable with a

> bare hand) while left side is more loose.. but there

> is no free play or wiggle in either joint (BTW i've

> pretty wimpy hands too).  there's still clean grease

> in both joints.  it's hard to tell if they're too loose

> at speed since the rubber front/rear mounts were

> rotted.

>

> the dust boots are cracked and rotted and they're

> not avail. from dealer apparently.  can i get new

> boots&clips from the guys who rebuild A arms?  given

> the wear on the car would i be better off going ahead

> and getting 'em rebuilt and be done with it?  *should*

> both A-arms be done at the same time?

>

> thanks,

>

> eric dorman

> edorman@mindspring.com

----------------------------------------------------------------------

Subject: re: HP to Weight Ratio's

From: "Tony" <toeknee@brandx.net>

Date: Mon, 26 Apr 1999 16:17:43 -0700

X-Message-Number: 106

Interesting:

I saw 340HP and TQ to the wheels. At 15% loss that works out to be 400HP

and 400TQ.

My 1986 951 (non S) at 2998 lbs at 400HP works out to be  7.45lbs/HP.  Not

bad.  Plus I know for a fact that I've pulled approx. 60-70 lbs. out of the

car too.

If I factor that in the ratio works out to be 7.34lbs/HP (at the 60 lbs.

reduction).

I'll be turning up the boost and installing my (future) aftermarket

throttle body and intake manifold soon.  I think I could see 370HP to the

wheels in a month or so.  Should be interesting.  Gotta love my old clunker

130K mile 2.5!!! hehehehe

Tony Garcia

Arch Entertainment LLC

www.archwebdesign.com

Internet Solutions/Credit Card Processing

(818) 730-9691

----------

> From: Jim Demas <JDemas@earthlink.net>

> To: 924/944/968 <924/944@rennlist.org>

> Subject: [924/944] The Rocket... & Power/weight ratios

> Date: Monday, April 26, 1999 3:30 PM

>

> After seeing The Rocket yesterday (see post yesterday) just scream

through

> some esses... I got to thinking about the power to weight ratios of a

> number of cars...

>

> car			weight	hp	ratio lbs/hp

>

> The Rocket... 		814	143	5.692

>

> 911 Twin Turbo		3490	400	8.725

> Porsche 911 (996)		3080	296	10.405

> Porsche 951S		2998	250	11.992

> Graham Gillies'944T (est)	2998	500	5.996

>

> Ferrari 550 M		3725	485	7.680

> Lamborghini Diablo SV	3365	530	6.349

> ViperGTS		3380	450	7.511

>

> Pretty damn impressive, I'd say.   Also.. the Rocket has 11" Brembos in

> front and 10.5 in the rear... think it stops great?!  Though the stated

> acceleration figures on their website are just 4.4 and 10.01 to 60 and

100

> respectively...  these must be the most conservative figures I have ever

> seen.  This car is faster than that.. and through the corners.. I am not

> sure anyone could keep up. No kidding.   You had to be there and see the

> car to believe how quick it was accelerating and going through the

corners.

> Bryce and I were amazed...

>

> So... I am on a diet today.  I need less weight.. and more hp.

>

> -- Jim

>

> Jim Demas

> Hillsborough, California

> (650) 579-1407

>

> 1991 S2 Coupe... KristallSilberMetallic/Black

>

----------------------------------------------------------------------

Subject: Re: APE STAGE II question

From: "Scott" <slevy6@ionet.net>

Date: Mon, 26 Apr 1999 18:34:58

X-Message-Number: 107

APE should let you upgrade to the 2.7 and banjo......

----------------------------------------------------------------------

Subject: Re: Can I install a ZF limited slip in a non-limited slip trans?

From: Davidjalai@aol.com

Date: Mon, 26 Apr 1999 19:35:46 EDT

X-Message-Number: 108

>

>Subject: "Improving" an '87 951

>From: porsharacer@earthlink.net

>Date: Sun, 25 Apr 1999 13:9:2

>

>

>I recently purchased an '87 951 and replaced the turbo with a K26S.  The

>car was chipped by the previous owner about five years ago.  Now that I

>have an "S" spec. turbo, would it make sense to replace the chips?  Are the

>new chips any better?  Could I or should I use chips made for the '88 or

>'89 951 that had the bigger turbo?

>

>I would also like to add Limited Slip.  I have found that it would be nice

>at the tracks here in California.  I assume a non-LSD car can be fitted

>with an LSD tranny.  Are there any issues or specifics I need to consider

>to fit to my '87 951?  I.E. only certain years that would bolt up, must I

>have one from a 951, etc.?

>

Hello,

I added a ZF limited slip from a 944 NA to my 1986 951. You will need

to have the diff housing machined to accept the drive gear for the trans oil

pump/cooler loop. I had Autothority do teh machining/install for me.

One note though....  the ZF diff uses wear discs for the friction

material. These discs have "917" part numbers - YES - they are from teh old

race-days!! But Porsche no longer makes teh 917 part.SO the new wear/discs

has a 951 part number. The new wear/friction discs are thicker. You will also

need new end caps for the diff housing...  The discs (If I remember

correctly!?) sell for $60 for each side, and teh end caps were $150 each (you

need one for each side!) - so just know that you will need some new parts to

make a used diff work!

BTW - If I was you... I would inspect which chips your car has. APE does make

K26/8 chips for an early car - like yours - that has the turbo-S turbo

installed. You want to make sure your engine isn't running too lean with the

wrong chip set!!

Good Luck

David Jalali

86 951

----------------------------------------------------------------------

Subject: Re: Changing the mini-thermostat: direction!?

From: Davidjalai@aol.com

Date: Mon, 26 Apr 1999 19:36:03 EDT

X-Message-Number: 109

>Subject: Dumb Question

>From: Mike427@aol.com

>Date: Sun, 25 Apr 1999 22:01:32 EDT

>

>

>	While changing the waterpump today I also decided to change both

>thermostats. The problem is the small one dedicated for the Turbo fell out

>and I am not sure which way it was installed. So which way is it, the long

>end (spring) in the pump, or in the plastic housing?

>

> Thanks in advance

>   mike427@aol.com

>       87 944T

>

Hello Mike,

The mini-thermostat for all 944 turbos - goes into the plastic elbow

"thing-y"!  The factory workshop book is inncorrect - it says it goes into

teh water pump. But it DOES NOT!  My Porsche factory tech buddy told me this.

Good Luck

David Jalali

86 951

----------------------------------------------------------------------

Subject: Re: Front wheels cause steering wheel to shake slighthly	at 100kph

From: FreitasRJ@aol.com

Date: Mon, 26 Apr 1999 19:39:09 EDT

X-Message-Number: 110

In a message dated 4/26/99 6:29:33 AM EST, agoolab@dtt.co.za writes:

<< My steering wheel seems to shake slightly at speeds between 100 and 110

kph. It stops shaking at speeds above and below those mentioned. I have had

the wheels aligned and balanced. Is there anything else I need to do to

stop this? Thanks in advance. >>

At this speed this is a classic case of wheel balancing.  Don't believe that

just because you had the wheels balanced that all is well.  I had to have

mine done three times before they got it right ..... there's alot of

technique involved beyond just tacking on weights where the machine tells

them to.  Have it re-checked.

Good luck,

Rich  (FreitasRJ@aol.com)

'84 944na  hellbronzemetallic

Smooth as glass now.

----------------------------------------------------------------------

Subject: Re: Front wheels cause steering wheel to shake slighthly	at 100kph

From: BadBob951@aol.com

Date: Mon, 26 Apr 1999 19:57:28 EDT

X-Message-Number: 111

In a message dated 4/26/99 6:29:41 AM Central Daylight Time,

agoolab@dtt.co.za writes:

<< My steering wheel seems to shake slightly at speeds between 100 and 110

kph. It stops shaking at speeds above and below those mentioned. I have had

the wheels aligned and balanced. Is there anything else I need to do to

stop this? Thanks in advance. >>

Have the runout checked (I think that's what it's called).  I'ts a

measurement of the out-of-roundness of the tire on the wheel.  Usually, if

this is the problem, remounting the tire after moving it 90 degrees on the

rim will do it.  For a better explaination of teh phenonenon, go to the tire

racks web page (www.tirerack.com).  If your tires are jsut to bad out of

round, you may just be SOL.

Bob

'86 951

blk/bkl

----------------------------------------------------------------------

Subject: 1986 944 For Sale

From: My83944@aol.com

Date: Mon, 26 Apr 1999 19:45:51 EDT

X-Message-Number: 112

OK Guys - I looked at this one today.

1986 Porsche 944, Color was the same, but a little darker than my Sienna red

Metallic, perfect body in every way, perfect interior in every way, less than

31,000 original miles, 2 owners, only modifications seem to be a stainless

Borla type exhaust, inlaid center caps (on 16" Fuch alloys) and a Turbo

valence (spelled right ?). Option codes are CO2, 395, 431, 456, 650 & 946.

Color code is LM3Y. This car is perfect. Oh, the asking price - - - - -

$16,900.00 Yes, Sixteen Thousand, Nine Hundred Dollars.

You can e-mail me if you want it -

Steve

Loving my 83 more and more every day, dings and all !

----------------------------------------------------------------------

Subject: 1986 911 for Sale

From: Matthew Murray <mattm@optonline.net>

Date: Mon, 26 Apr 1999 20:26:26 -0400

X-Message-Number: 113

All:

A net impaired friend has a 911 for sale

PLEASE, contact him directly.

It is a blue '86 Targa

WP0EB0918GS161464

AC

CD player

Manual trans

New steering rack

Leather interior

Whale tail

Power windows, locks, seats

Cruise control

67,000 miles

Asking price is $16,999.00

Call 860-828-0197

The car and owner are in central Connecticut.

I have no financial interest and other disclaimers,

and I DID try to talk him out of it.

--

Matt Murray

My home e-mail now is mailto:mattm@optonline.net

It was mattm@nassau.cv.net

Please note the change in your address books

As always, work is:

mailto:mdmurray@gwns.com

----------------------------------------------------------------------

Subject: Re: 1986 944 For Sale

From: James Webb <jw944@usa.net>

Date: Mon, 26 Apr 1999 20:30:11 -0400

X-Message-Number: 114

>less than 31,000 original miles, 2 owners, only modifications seem to be a

stainless

>$16,900.00 Yes, Sixteen Thousand, Nine Hundred Dollars.

Am I the only one who thinks low mileage and high price do not correlate

on an aged car?  It seems to me that at only 31k miles in 13 or 14 years,

the seals will be dry and leaking, and several maintenance things (e.g.

brake fluid) will probably have been overlooked.  I'm also concerned about

corrosion in the bearings.  I'd rather have a high-mileage Porsche, at

least then you know it's been running.  And that's what you want it to do.

IMHO.

James

87 Gold 944

----------------------------------------------------------------------

Subject: Link to your car website              TonyG's website

From: "Tony" <toeknee@brandx.net>

Date: Mon, 26 Apr 1999 17:37:55 -0700

X-Message-Number: 115

If anybody out there would like to link up car sites, please email me with

your URL and name and I'll put it up on my website.

A reciprocal link would be appreciated.

My website is at: http://modigliani.brandx.net/user/toeknee/index.html

Thanks,

Tony Garcia

Arch Entertainment LLC

www.archwebdesign.com

Internet Solutions/Credit Card Processing

(818) 730-9691

----------------------------------------------------------------------

Subject: straightening a bent wheel

From: Don Bredle <bredledl@uwec.edu>

Date: Mon, 26 Apr 1999 18:43:26 -0600

X-Message-Number: 116

I've got a small bend on the inner lip of one of my phone dial rims (8x16

original). The rim is bent in only a couple millimeters by 2 or 3 inches in

length. Just enough to see it pinching in the tire when mounted. Is there

any functional worry with this little bit of bend? Do I dare attempt to

straighten this out myself, or do these things crack when hammered or

clamped?  If I'm bound to break it, who does this kind of "minimal"

straightening. Anybody in the Twin Cities area?

Thanks.

Don Bredle

Eau Claire     '88 951

----------------------------------------------------------------------

Subject: Re: straightening a bent wheel

From: "Mike" <mwgildea@fast.net>

Date: Mon, 26 Apr 1999 20:43:25

X-Message-Number: 117

Don,

Don't know anything about straigtening wheels or the possible side effects.

I do know that there is an outfit in Bath, PA that does this kind of work.

It's the only one I've ever seen advertised (maybe because I live in

NJ/PA).  Don't know anything more about them or have any experience.  Their

website is www.wheelcollision.com.

MG

----------------------------------------------------------------------

Subject: saw a nice shiny 944 cabriolet today

From: grouchy@ce.mediaone.net

Date: Mon, 26 Apr 1999 21:02:15 -0500 (CDT)

X-Message-Number: 118

I was heading home from work I90/94 north just by addison in the

midst of the beautiful evil empire (aka chicago) when a white 944

convertible passed me.  It appeared to head off on the montrose

exit.

Appeared to be a cream white, no badge in the back, black soft

top.

(Just wanted to spam^H^H^H^Hshare that 'ooh neat' stuff)

-Brent

'87 Kalahari Gold 951 (still up on blocks unfortunately)

----------------------------------------------------------------------

Subject: Re: bellhousing help

From: Robert Cohn <rwcohn@mcs.net>

Date: Mon, 26 Apr 1999 21:04:59 -0500

X-Message-Number: 119

I made a puller using a piece of pipe just over the length of the pivot

shaft,

a stack of washers, several pieces of small I.D. pipe cut to different

lengths,

a length of threaded stock about twice the length of the pivot shaft,

and a nut.

The small I.D. pipe pieces are not absolutely needed.

While using this tool I realized that if I were to have made a cutter to

accurately cut a flat pad around the end of the pivot shaft, the puller

wouldn't have cocked to one side.  I even took measurements so I could

make the tool on my lathe, if I needed to do the job again.  Or if

somebody made it worth my while.

Unless the car you are working on is spotless, this tool works better

than the beat on a pair of  Vice Grips clamped onto a bolt that has been

threaded into the end of the pivot shaft method.

Just another special tool I hope I don't need to use again.

Happy Motoring

Mine is totaled and I'm looking for another.

With parts unbolted and the inner structure more exposed, the shop found

some damage that they hadn't seen before.  Ouch!

Rob Cohn  -  Porscheless for now, but not forever.

john anderson wrote:

> You have to pull that pin all the way out...I used vice grips and a

> hammer to bang it down and

> out.. its about 6" long if I remember....It was very frusterating to

> have the housing that loose

> only to have it held in place by that one damn pin.

>

> John

>

> Ray Colombo wrote:

>

> > We're working on a clutch for an '86 951, it's going fairly well,

> but

> > slow. We are at the bellhousing, it is loose but won't come off. How

> far

> > does the release lever pull out, I have it out about 3". What else

> can

> > be holding the bellhousing? Help! Any other tips greatly

> appreciated.

> >

> > Thanks,

> > Ray Colombo

> > '89 951 working on Dan Webb's '86

>

>

----------------------------------------------------------------------

Subject: S2 Throttle Bodies

From: Jim Demas <JDemas@earthlink.net>

Date: Mon, 26 Apr 1999 19:51:06 -0700

X-Message-Number: 120

Has anyone run one of the S2 enlarged throttle bodies?

Whose unit?

How pleased were you with it?

Thanks.

-- Jim

Jim Demas

Hillsborough, California

(650) 579-1407

1991 S2 Coupe... KristallSilberMetallic/Black

----------------------------------------------------------------------

Subject: Re: Name That Place Winners

From: "Trent Duff" <tduff01@mail.win.org>

Date: Mon, 26 Apr 1999 21:55:8

X-Message-Number: 121

Ahem.  It took me a few seconds to think of it.  The Skyline and Blue Ridge

Parkway are great roads I look forward to return to in my 944S.  The roads

south of the Smokies National Park are must see, according to this post, I

hope to allow time for that next time we are there.

Yes, this is a great road for the Porsche car, however you must have self

control.  The rangers are sometimes ready for fast drivers and I don't know

what they need the money for, but it must be a good cause....

Also want to go through Rocky Mountain National Park in Colorado in my

P-car.  Must watch the speed limit though.  I followed a 911 going fast at

dusk.  We were lucky, or the rangers were eating dinner.  Also watch out

for HUGE Bambi that will make road kill of your baby.

;-)

Trent

----------------------

On 04/26/99, ""raceone" <raceone@email.msn.com>" wrote:

> Congratulations to the two winners of the Name That Place Challenge! Their

> responses are reprinted below just in case you missed them yesterday.

>

>

> >Subject: Re: Name this Place

> >From: "Trent Duff" <tduff01@mail.win.org>

> >Date: Sun, 25 Apr 1999 15:56:12

> >X-Message-Number: 39

>

> >>On 04/25/99, ""raceone" <raceone@email.msn.com>" wrote:

> > >Test your knowledge of Great Porsche Roads:

> > >

> > >One road, no straights longer than 1/2 mile, no stop signs or lights, no

> > >towns, no houses or driveways, no commercial vehicles, no businesses

> (other

> > >than a few "rest areas" with gas and food), NO traffic (went 42 miles in

> > >April without seeing ANY cars and only passed 3 cars going my way in 200

> > >miles), constant elevation changes, all turns were 3rd/4th gear (oh,

> there

> > >were a couple 2nd gear turns but 5th gear was useless), oh and it's 560

> > >miles long!!

>

> >Skyline Drive along the Appalachian Trail.  If that's not it, its a whole

> lot like it. Scenery is spectacular.  >Nothing but woods and curves.  Nice

> road, too.  If you drive south in Virginia it gets better as you go, the

> >mountains get taller. Its a thrill to drive.  Not as steep as Colorado

> highways, but you are in a park in the >northern part, so traffic is not as

> bad and you don't have granite chunks all over the road waiting to rip your

> >tires.

> >Trent

>

> Actually, it is the northern most 100 miles of this route in Virginia

> located in the Shenandoah National Park (entrance fees apply) that is called

> Skyline Drive. It connects directly to the Blue Ridge Parkway at

> Waynesboro/I-64 which goes another 460 miles and ends at the eastern

> entrance to the Smokey Mountains National Park.

>

> A few addition considerations include the Skyline Drive portion carries a

> ridiculous 35 mph speed limit and the Parkway portion has a 45 mph speed

> limit, and I'm sure these roads are clogged with motorhomes and higher

> traffic volumes during the peak vacation travel months during the summer.

> There are also VERY few legal passing zones, but many perfectly safe

> opportunities exist (particularly with a Turbo) if you ignore the double

> yellow lines. The road is patroled by Rangers who have the power to write

> citations but I only saw one during my entire time on both sections and he

> used an old X-band moving radar that was just left on -- nearly any detector

> would easily provide ample warning if he is typical.

>

>

> >Subject: Re: Name this Place #2

> >From: "randy cook" <rmcooks@earthlink.net>

> >Date: Sun, 25 Apr 1999 17:30:53

> >X-Message-Number: 42

>

> Denny wrote:

> >>One road famous with motorcylcists that has 318 turns in 11 miles and lays

> >>claim to being the "Curviest Road in America".

>

> >>I turned around and drove is back again making for 636 turns in 22 miles!!

> >>You know how sections of road can be "adopted" and signage put up -- well

> >>this one is adopted by a local sports car club... Imagine that!!!!

>

> >>Again, post your responses to the list.

>

>

> >the road is called deals gap or ride the dragon. ive riden up there for

> >years and its fricken awsome. but be careful of the road has some history

> >ride the dragon and it will bite some times

>

> I would like to add to Randy's description of Deal's Gap, aka "The Dragon"

> that it is US129 located on the North Carolina/Tennessee border just south

> of the Smokey Mountains National Park. As awsome as this road is, there are

> MANY other incredible but slightly less intense roads throughout this area

> including NC Route 28 that also deserve the attention of your Porsche. If

> you're looking for a road trip destination....

>

> Take care.

>

> Denny

>

> Raceone@email.msn.com

> PCA - Rally Sport Region

> BMWCCA #168191

> Detroit, Michigan

>

> '88 - 951S

> '95 - 540i 6-speed

> '98 - ML320

> '95 - VW Cabrio (daughter Christine's)

> '92 - KTM 300

> '92 - KTM 250 (son Kevin's) -- (Colorado trails in August)

>

> Anyone notice a slightly Germanic theme......

----------------------------------------------------------------------

Subject: Re: straightening a bent wheel

From: "Willard Bridgham 3" <willard3@albany.net>

Date: Mon, 26 Apr 1999 22:8:8

X-Message-Number: 122

Send the damn wheel out and get it fixed. The only thing you can do with

the tools you have is make it worse. Plus, DON'T GO FAST on a bent wheel.

----------------------------------------------------------------------

Subject: Need A Pep Talk!

From: "al comeaux" <apcomeaux@aol.com>

Date: Mon, 26 Apr 1999 22:9:25

X-Message-Number: 123

Hi All!  Just picked up my 86 951 from the mechanic after spending $800 to

get my A/C fixed. After reading several posts on the market value of our

cars and people getting flamed for asking $12,000 for a 13 year old car,

why do we continue to pour money into them.  I paid $9,300 two years ago

and have already spent $4,000 in repairs (Clutch, motor mounts, A/C

compressor, oil leaks, tires) and now a high pressure line for the A/C. I

know that I have a car that I have $13,000 invested that will out perform

and out handle almost anything on the road. Then, why should I not be able

to get that amount from some lucky buyer?  I just don't know when I should

stop putting money into it. I am not sure if I should sell it and buy

something a little more reliable or keep sinking my hard earned money into

it. My daughter has a 87 Honda Accord with 190,000 miles on it and it is

never in the shop for anything. All feedback is welcome. Both good and bad,

I just want someone elses opinion.

Al Comeaux  86 951 Blk/Blk

----------------------------------------------------------------------

Subject: Building a new car?

From: Bill Catchings <catching@telapex.com>

Date: Mon, 26 Apr 1999 22:11:29 -0500

X-Message-Number: 124

P-Fiends,

As you may or may not know, my son totaled our '84 944 at Easter with no

injury to himself.  I am now considering what it will take to utilize

the good mechanical parts of the '84 in another 944 body to create a new

car for him.  Why I am even considering this, I don't know.  Dr. Steve

has advised me that I would need a new wiring harness to put the '84

mechanicals into a newer body.  Couldn't I just transplant the DME also?

Can you folks give me some idea of the obstacles I will be facing in

transplanting a pre '85.5 engine/drivetrain into a newer style body.

Should I give up this fantasy, and the 2 week old clutch in the '84?  I

need advice from the collective.  Any and all comments are welcomed and

appreciated.

TIA,

Bill

----------------------------------------------------------------------

Subject: Re: 944 Turbo SE Silver Rose 1988 RHD

From: "Willard Bridgham 3" <willard3@albany.net>

Date: Mon, 26 Apr 1999 22:19:2

X-Message-Number: 125

Known, to me at least, as Rose Rocket, the 88 952 limited edition has about

total of 1000 copies, only 750 sold in US. I have one which dynoed at 290

hp, bone stock but for test pipe. All other specs but for color and

upholstery and interior trim are same as other 88 and 89 952's. Buy the

tech spec book from Porsche.

----------------------------------------------------------------------

Subject: Re: 944 Story...

From: "Willard Bridgham 3" <willard3@albany.net>

Date: Mon, 26 Apr 1999 22:26:45

X-Message-Number: 126

RE: oil leaks from engine. Get your money together and go have your local

mechanic replace ALL THE SEALS ON THE FRONT OF THE ENGINE. Cost about

500-1000, but it's the only way to tell it's not air-cooled, it doesn't

leak oil. Seals seem to harden and leak in about 10 years, not all that

bad.

----------------------------------------------------------------------

Subject: Re: Synthetic Oil

From: thomas.pultz@lightmail.com (Tom Pultz)

Date: Tue, 27 Apr 1999 03:29:26 GMT

X-Message-Number: 127

On Mon, 26 Apr 1999 18:2:38, "Nabi" <nabi@vill.com> wrote:

>15W-50 would be better in the hot summer months.

If someone is using a high quality synthetic motor oil there isn't really

any need for 15W50 for normal use.  The use of too high an oil viscosity

will actually make the oil run hotter because of increased friction in =

the

bearings.  I've been using Red Line 10W40 in my S2 and even on the track =

it

uses no oil.  My son also uses it in his '89 turbo with similar results. =

I

think 10W30 should be just fine if your engine is in a good state of =

repair,

i.e., uses little or no oil in between changes.

>On 04/26/99, ""alex loureiro" <alexloureiro@email.msn.com>" wrote:

>> Living in the northeast where the temp varies by season, what grade =

mobile

>1 should be used. In the summer months is 15w-50 the choice or is 10w-30=

a

>better one?

>

>Alex-'88 944 Turbo S

Tom Pultz <thomas.pultz@lightmail.com>

Redmond, Washington, USA - Pacific NW Region PCA

'90 944 S2 Coupe, Guards Red/Black

'89 944 Turbo, Guards Red/Linen - son Scott's

----------------------------------------------------------------------

Subject: Re: Overheating...End of the line!

From: "Willard Bridgham 3" <willard3@albany.net>

Date: Mon, 26 Apr 1999 22:34:0

X-Message-Number: 128

Low octane gas has lower flash point (burns at lower temp). Higher octane

has higher flash point (burns at higher temp). Changing gas to high zoot,

all other things held constant, increases engine temperature.

----------------------------------------------------------------------

Subject: Re: 1986 944 For Sale

From: STG944@aol.com

Date: Mon, 26 Apr 1999 21:33:20 EDT

X-Message-Number: 129

In a message dated 4/26/99 8:19:26 PM Central Daylight Time, My83944@aol.com

writes:

<< $16,900.00 Yes, Sixteen Thousand, Nine Hundred Dollars.

You can e-mail me if you want it - >>

Get real!  Tell that guy to have fun selling the car at that price.  Take

your 16.9 and find a late model turbo.

Tim Matta

PCA Chicago

----------------------------------------------------------------------

Subject: Re: MAF conversion

From: "Willard Bridgham 3" <willard3@albany.net>

Date: Mon, 26 Apr 1999 23:4:0

X-Message-Number: 130

Ya gotta' measure the airflow somehow. The MAF (mass air flow) sensors are

just hot wire anemometers as opposed to the stock plate. Stock plate has

big cross-section, hot-wire doesn't. More air, hotter fire.

----------------------------------------------------------------------

Subject: for sale trade(924 guages)

From: "adam" <jusadam@aol.com>

Date: Mon, 26 Apr 1999 23:5:14

X-Message-Number: 131

my 85(early)944 came with 924 guages, black with white numbers, i now have

the right ones, black with yellow.  im selling the others all work fine but

the odometer doesnt(whats new). willin to trade for something else if u got

something or make me an offer

----------------------------------------------------------------------

Subject: Re: heater stays on

From: "Willard Bridgham 3" <willard3@albany.net>

Date: Mon, 26 Apr 1999 23:7:58

X-Message-Number: 132

A thing other than the heater valve to check is the operation of the

dampers. Sometimes the damper control doesn't work and stays open to the

coils.

----------------------------------------------------------------------

Subject: Re: Cam belt cover on '84 944 NA

From: "Dave Nelson" <corwin@inetnebr.com>

Date: Mon, 26 Apr 1999 23:22:39

X-Message-Number: 133

Your mechanic is right.  When you put in the upgraded water pump there is a

new guide that is added to keep the cam/water pump/crank belt from slapping

against the water pump pully.  This slapping motion may have contributed to

many of the older water pumps going out and leaking around the seals of the

water pump shaft.  I had to modify the cam/ballance shaft cover to get the

belt to stay within this guide.  There was a drawing with the upgrade water

pump kit that shows what needs to be taken out.  A Dremel tool, or small

grinder works great on it.

----------------------------------------------------------------------

Subject: Re: Need A Pep Talk!

From: TCThomas77@aol.com

Date: Tue, 27 Apr 1999 00:04:46 EDT

X-Message-Number: 134

In a message dated 4/26/99 8:12:06 PM, apcomeaux@aol.com writes:

<<  I know that I have a car that I have $13,000 invested that will out

perform

and out handle almost anything on the road. Then, why should I not be able

to get that amount from some lucky buyer?  I just don't know when I should

stop putting money into it. I am not sure if I should sell it and buy

something a little more reliable or keep sinking my hard earned money into

it. My daughter has a 87 Honda Accord with 190,000 miles on it and it is

never in the shop for anything. All feedback is welcome. Both good and bad,

I just want someone elses opinion. >>

Al:

My cousin the car salesman used to say "there's an a$$ for every seat."

Maybe you could get someone to pay that much for it, but don't confuse the

amount you have invested in the car with its value.  One of the things I like

about our cars is the incredible bang for the buck they provide.   I got out

of my 1988 911 in favor of my S2 because the S2 was just a better all around

car and better for me for the track, given my skill level .  It cost half as

much as I got for the 911.

My wife's Honda has 160K on it, and it is never in the shop either.  But it's

just an appliance.

Terry Thomas

1989 944S2

----------------------------------------------------------------------

Subject: Re: Building a new car?

From: "Scott A. Harrison" <Scott.Harrison@telmon.com>

Date: Mon, 26 Apr 1999 23:36:30 -0500

X-Message-Number: 135

Honestly, I think you would be ahead moneywise and hasslewise to part out

the 84 and put the money towards a newer car.  Much as I hate to see another

'84 pass on to the great Autobahn in the sky, considering the rather small

investment it takes to get a newer style NA in decent running condition, I

can't imagine you would do any better buying a shell and trying to make the

pieces fit.  Unless, of course, you are going to make your son do all the

work as a punishment for totalling your '84.  :)

Regards, ...Scott

----- Original Message -----

From: Bill Catchings <catching@telapex.com>

To: 924/944/968 <924/944@rennlist.org>

Sent: Monday, April 26, 1999 10:11 PM

Subject: [924/944] Building a new car?

> P-Fiends,

>

> As you may or may not know, my son totaled our '84 944 at Easter with no

> injury to himself.  I am now considering what it will take to utilize

> the good mechanical parts of the '84 in another 944 body to create a new

> car for him.  Why I am even considering this, I don't know.  Dr. Steve

> has advised me that I would need a new wiring harness to put the '84

> mechanicals into a newer body.  Couldn't I just transplant the DME also?

>

> Can you folks give me some idea of the obstacles I will be facing in

> transplanting a pre '85.5 engine/drivetrain into a newer style body.

> Should I give up this fantasy, and the 2 week old clutch in the '84?  I

> need advice from the collective.  Any and all comments are welcomed and

> appreciated.

>

> TIA,

>

> Bill

>

>

>

> +++

>

> The 924/944 list is sponsored by dC Automotive

> http://www.dcautomotive.com or 800-579-2410 or Rob@dcautomotive.com

> Our Sponsors Support this list- so Please support them (Rennlist Members

receive a discount!)

>

> ___

> You are currently subscribed to 924/944 as: Scott.Harrison@telmon.com

> To unsubscribe send a blank email to leave-924/944-10643U@rennlist.org

>

>

----------------------------------------------------------------------

Subject: Re: Use of radars abroad.

From: TCThomas77@aol.com

Date: Tue, 27 Apr 1999 00:17:07 EDT

X-Message-Number: 136

In a message dated 4/26/99 4:54:51 AM, ChristianStewart@compuserve.com writes:

<< Can guarantee the weather here in Scotland though, rain, with more rain,

occasional sleet and snow with sudden spells of glorious sunshine so

infrequent as to be spoken about in awe over a beer in the pub.....the only

consolation being that fixing the broken sunroof really isn't a pressing

problem....:~) >>

Hmm.  Sounds like Seattle.

Terry Thomas

1989 944S2

----------------------------------------------------------------------

Subject: Re: Sparco Seats....

From: "Claus Groth" <bora450@gte.net>

Date: Mon, 26 Apr 1999 21:38:44 -0700

X-Message-Number: 137

Kyle wrote:

<< Can some one suggest a place that I can get a set of SPARCO Super Sport

seats.  I am sick of the basic seats I have in there now, they do not let me

drive, they make me spend my time trying to stay in the seat... >>

Call Galan at WERKS II, Glendale CA.  He advertises in Excellence.  I can

find the telephone number if you can't find it.  Galan supplies mounting

brackets that adapt the seat to slide rails that mount at the existing seat

rail locations.  This makes for an easy swap.  It takes me ten to fifteen

minutes to replace the seat.  I'm just a happy customer.

Claus Groth, '86 951, bora450@gte.net

Subject: [racing] Re: Race Seat, 4/13/00

From: "Barry Lenoble" lenobleb@symbol.com

I can second Jeffrey's views on Kirkey seats. I have one, and I love it - for track events. IMHO, for regular use, it would be a real pain. However, for track use, you can't beat it for cost, safety, strength, ease of installation, etc. They are tough to get into and out of, ESPECIALLY if you have a roll cage. I've managed a specific routine to get in and out. I get a laugh every time I take some one for a ride, and I watch them figure out how to climb in.

One final comment, the seats come in various widths, so you should not be 'squeezed' in one. I use a 14.5" one for me, but I'm not that big (5' 7", 165 lbs). For my passenger seat, I have a 17" seat. My friend who is 6' 3" and 250 minimum fits just fine. In fact, he ordered the same size seat for himself.