NEMA Plug and Receptacle Descriptions

Please refer to the following drawings to distinguish between various plug and receptacle types.

- Each drawing can be considered both a Plug "P" or Receptacle "R".

- The "L" refers to the Locking feature of the plug or receptacle.

- The first number represents the voltage: 5 = 120 VAC 6 = 208/240 VAC.

- The second number represents the current: for example 15 = 15 Amps

|  | 5-15P | 5-15R |  |  | L5-15P | L5-15R |
| --- | --- | --- | --- | --- | --- | --- |
|  | 5-20P | 5-20R |  |  | L5-20P | L5-20R |
|  | 5-30P | 5-30R |  |  | L5-30P | L5-30R |
|  | 5-50P | 5-50R |  |  |  |  |
|  | 6-15P | 6-15R |  |  | L6-15P | L6-15R |
|  | 6-20P | 6-20R |  |  | L6-20P | L6-20R |
|  | 6-30P | 6-30R |  |  | L6-30P | L6-30R |
|  | 6-50P | 6-50R |  |  |  |  |
|  | 14-30P | 14-30R |  |  | L14-30P | L14-30R |

2-Pole 2-Wire 15 Amp 20 Amp 30 Amp 50 Amp 60 Amp 125 Volt NEMA L1-15 N/A N/A N/A N/A 250 Volt N/A NEMA L2-20 N/A N/A N/A 277 Volt AC N/A N/A N/A N/A N/A 600 Volt N/A N/A N/A N/A N/A

2-Pole 3-Wire Grounding 15 Amp 20 Amp 30 Amp 50 Amp 60 Amp 125 Volt NEMA L5-15 NEMA L5-20 NEMA L5-30 NEMA L5-50 NEMA L5-60 250 Volt NEMA L6-15 NEMA L6-20 NEMA L6-30 NEMA L6-50 NEMA L6-60 277 Volt AC NEMA L7-15 NEMA L7-20 NEMA L7-30 NEMA L7-50 NEMA L7-60 347 Volt AC N/A NEMA L24-20 N/A N/A N/A 480 Volt AC N/A NEMA L8-20 NEMA L8-30 NEMA L8-50 NEMA L8-60 600 Volt AC N/A NEMA L9-20 NEMA L9-30 NEMA L9-50 NEMA L9-60

3-Pole 3-Wire 15 Amp 20 Amp 30 Amp 50 Amp 60 Amp 125/250 Volt N/A NEMA L10-20 NEMA L10-30 N/A N/A 3Ø 250 Volt NEMA L11-15 NEMA L11-20 NEMA L11-30 N/A N/A 3Ø 480 Volt N/A NEMA L12-20 NEMA L12-30 N/A N/A 3Ø 600 Volt N/A N/A NEMA L13-30 N/A N/A

3-Pole 4-Wire Grounding 15 Amp 20 Amp 30 Amp 50 Amp 60 Amp 125/250 Volt N/A NEMA L14-20 NEMA L14-30 NEMA L14-50 NEMA L14-60 3Ø 250 Volt N/A NEMA L15-20 NEMA L15-30 NEMA L15-50 NEMA L15-60 3Ø 480 Volt N/A NEMA L16-20 NEMA L16-30 NEMA L16-50 NEMA L16-60 3Ø 600 Volt N/A N/A NEMA L17-30 NEMA L17-50 NEMA L17-60

4-Pole 4-Wire 15 Amp 20 Amp 30 Amp 50 Amp 60 Amp 3Ø Y 120/208V N/A NEMA L18-20 NEMA L18-30 N/A N/A 3Ø Y 277/480V N/A NEMA L19-20 NEMA L19-30 N/A N/A 3Ø Y 347/600V N/A NEMA L20-20 NEMA L20-30 N/A N/A

4-Pole 5-Wire Grounding 15 Amp 20 Amp 30 Amp 50 Amp 60 Amp 3Ø Y 120/208V N/A NEMA L21-20 NEMA L21-30 NEMA L21-50 NEMA L21-60 3Ø Y 277/480V N/A NEMA L22-20 NEMA L22-30 NEMA L22-50 NEMA L22-60 3Ø Y 347/600V N/A NEMA L23-20 NEMA L23-30 NEMA L23-50 NEMA L23-60

IEC_309

IEC-320-C20 (16A)Mates to IEC-320-C19

IEC-320-C14 (10A)  Mates to IEC-320-C13